Track and Field Equipment

Specifically; Javelin, Discus, Vaulting Poles

- Discus

A.     Performance/Flight Parameters

i. Flight Distance

      - Speed of Discus at Release

      - Angle of Release

      - Height of Release

      - Lift

        - Positive angle of attack

        - Gyroscopic Effect

        - Spin Rate versus Rim Weigh

        - Stable flights require athlete to achieve adequate spin rates related to rim weight

B.      Design Parameters

    - Reported rim weights by Manufacturers = 2kg model

    - 1.6kg models 4% to 6 % less from high to low moment

    - 1kg models  6% to 8% less from high to low Moment

    - Higher rim weights equal more fragile plates

II.    Javelins

- Performance/Flight Parameters

  - Flight Distance

      - Speed of Javelin at Release

      - Height of Release

      - Angle of Release

        - Mechanical best versus human body best

        - Everyone is different

      - Angle of Attack

        - Higher better up to a point

        - Higher requires more speed to maintain flight

        - Caused by Asymmetrical profile

      - Lift

        - Surface area

        - Angle of Attack

        - Oscillations

i.      Most lift at release javelin has most speed

ii.     Changes in flight from + to – angle of  attack

iii.    High moment versus low moment

iv.    High moment easier to control

v.     Low moment spends more time in + angle of

attack

      - Drag

        - Shape of the final 6” of the tail smaller better

        - Vibration causes drag

- Rapid dampening best

- Stiffer better, but higher injury potential

      - Point types

        - Sharp point

- Less lift

- Corrects missed throws better

        - Blunt Points

- More Lift

- Will not correct missed throws

        - Rubber tips

- Most lift of any point

  - Design Parameters

1,   Angle of Attack

      - Maximize by largest diameters in front of the grip and smallest diameters behind grip within  the rules

- Front of grip 30mm men, 25mm women

- Back of the grip no more than .25mm smaller than front

- Front mid point smaller than 90% of front of grip

- Rear mid point larger that 90% of  front of the grip

      - Moment of inertia

- Low moment allows for quicker attainment angle of attack

- Low moment allows more time in best angle of attack

- Lift

a.   Surface area

b.  Grip

c.  Vibration

i.  Aluminum versus steel versus Carbon

D.    Construction

i. “O” or soft tubing

ii. Taper machine

- Tails

- Fronts

iii. Heat Treat and Age

iv. Sanding

1. Weight

2,  Balance

3. Diameters

v.         Paint or Anodize

vi.        Attach point

vii.        Wrap Grip

- Decals

- Final Straighten

III.  Vaulting Poles

  - Performance Parameters

    - Bending Poles to shorten Radius of Rotation

    - Poles to Return Energy

    - Pole Diameter For Good Grip

    - Pole Carry Weight

  - Pole Characteristics

    - Stiffness

      - Diameter: Most important – Larger = Stiffer

      - Wall Thickness: Thicker = Stiffer = Heavier = Safer

      - Modulus of elongation

        - Weave type – Bi-directional  versus Uni-directional

        - E-glass

        - S-glass

        - Carbon

    - Design

      - Inner Wrap – Hoop Strength

1.  Bi-Directional

2.  Spiral Wrap

3.  History

      - Body Piece

        - 2-3-4 Plys or wraps

        - E-Glass versus S-Glass versus Carbon

      - Sail Piece – Trapezoid

        - To strengthen Center of the Pole

        - Create Circular Bend

        - Height of Bend: higher is harder to rotate in but lifts vaulter higher

      - Soft Side

        - Rail Effect

        - Added Stiffness/Performance of Pole

      - Pole Flex

        - Flex Chart

        - Procedure

i.     Support Positions

ii.    Weight & its Placement

iii.   Beam Theory

iv.    Sail Piece dimensions

v.    Interpreting Chart and Relating Poles

iii.   Construction

- Patterns

Glass Types/Pre Preg

- Wrapping Mandrels

1.  Mandrels

2.  Machines

3.  Patterns/order

- Cooking

  - Oven construction

  - Steam

  - Air Pressure

  - Resin cure – heat, time, pressure

  - Pole orientation

  - Pre-Bend

  - Blemishes

- Trim

- Bending Test

- Flex Test

- Finish

  - Pole plug

  - Pole cap

  - Tape

  - Decals